## Slide 1: Quickstart – DE4L Sensing App

## Slide 2: diGuRaL Sensing App
Google Play Store
https://play.google.com/store/apps/details?id=de.lll.digural.senseapp

## Slide 3: AirBeam 2
https://www.habitatmap.org/airbeam
Bluetooth Classic
PM1, PM2.5, PM10

## Slide 4: AirBeam 3
https://www.habitatmap.org/airbeam
Bluetooth LE
PM1, PM2.5, PM10

## Slide 5: Ruuvi Tag
https://ruuvi.com/
BLE Beacon
Temperature, Humidity, Air Pressure

## Slide 6: App – Permissions – Location / Bluetooth
App uses location services and within a foreground service when active - no hidden location tracking
  Select “Allowed only while in use” when asked for permission
App uses Bluetooth device discovery for sensor connection
  Select “Allow” when asked for permission
App needs to display a notification, so tracking is possible while app is in background
  Select “Allow” when asked for permission

## Slide 7: App – Link Sensor (only once)
Link Sensor sensor with app
Default scan is for BLE devices only
Enable Legacy Scan to scan for BT classic devices. Currently only needed for AirBeam2
Option 1
Option 2

## Slide 8: App – Connect Sensor
Press „Connect“ in „Devices“ screen
Connection process can last up to 60 seconds
When the sensor is connected the first time, a pairing notification might be shown by Android
On success, the app automatically switches to the „Home“ screen

## Slide 9
Use diGuRaL account to login
App – Login

## Slide 10: App – Start Tracking
Tracking can only be started when at least one sensor is connected and a user logged in

## Slide 11
1. Disconnect Sensor
  (Data transmission and tracking is stopped automatically)
2. Log out
  (Data transmission and tracking is stopped automatically)
3. Stop Tracking
Notification in status bar
4. Stop Tracking and disconnect sensor
1.
2.
3.
4.
App – Start Tracking
4.

## Slide 12
In case the connection to the sensor is lost unexpectedly, the app tries to reconnect
To cancel the reconnect trials, press the sensor „button“
App – Features – Reconnect

## Slide 13: Data transmission
The app transmits data to an MQTT Endpoint in real-time
Transmitted data includes sensor measurements, timestamp, location, username and the current app version.